## Slide 1
Waste Treatment BAT Conclusions Permit Reviews
PLEASE ENSURE YOU ARE ON MUTE!
SEPA Oct/Nov 2022

## Slide 2
What we will cover
1. Introduction to the new Waste Treatment (WT) BREF/ BATCs
2. Key changes
3. How permit reviews will work. This will include:
  Permit review mechanism and timescales
  Completion of BAT Gap Analysis in response to Reg 63(2) Notice
  Unconstructed and Mothballed sites
  The SEPA WT BATCs Interpretation Document
  Key differences between SEPA and EA approach
  New Permit Templates and other changes
4. Q&A session
(Format for questions: Please use the chat function)
Notes: Here is the agenda for the session. We will make the presentation available on our website.
This presentation is quite high level and generic. The purpose is to give you an overview of the BRef and the review process. Due to commercial confidentiality we can’t go into detail about specific site circumstances.
We will save questions until the end. Either put them in the chat as we go, if you think you might forget about it, or at the end if you want to wait and see if it is answered. We will also have a short "hands up" session if there is time.

## Slide 3
1. Introduction to the new WT BREF/BATCs (1)
Covers waste treatment by mechanical, biological and physico-chemical processes as well as temporary storage of hazardous waste
BRef note = BAT (best available techniques) reference note
Published by the European Commission – collaborative process via the Technical Working Group (Member States, industry representatives and NGOs) and Shadow TWGs at MS level
Ensures use of BAT, continuous improvement + consistency across EU
Main BREF document describes BAT; accompanying BAT conclusions (BATCs) set out standards which must be met
BAT-AELs form basis for new ELVs (unless operator obtains a derogation)
EU Exit - BATCs have been incorporated into UK law
Notes: The Waste Treatment BRef covers a wide range of waste activities under specific sections of the pollution prevention and control regulations, namely 5.3 (hazardous waste treatment), 5.4 (non-hazardous waste treatment including biological treatment and metal shredding), 5.6 (temporary storage of hazardous waste) and 5.7 (independently operated waste water treatment).
The process started way back in 2013 with the formation of an EU Technical working group which brought together representatives from government, trade bodies and NGOs across all European Member States. There was also a shadow UK working group to feed into these discussions. The process started with the nomination of reference plants- those which are considered to be the best in terms of environmental performance- and then data gathering to establish a baseline across Europe.
The output was a Best Available Techniques Reference Document (BRef) which describes the processes and technologies along with data on all aspects of plant operation and performance in use across Europe. It has a set of BAT conclusions which are standards which must be met, covering process design, management and performance. It also contains BAT AELs- associated emission levels- which form the basis for emission limit values which apply through permit conditions.
But why are we complying with a European requirement if we have left Europe? Principally because the Waste Treatment BRef was agreed and published in 2018 it will be implemented as part of the exit agreement. Future BRefs may be done differently and there is a UK group working on how BAT will be developed across the UK.

## Slide 4
1. Introduction to the new WT BREF/BATCs (2)
BATCs published 10/08/18 – 4 years for existing plants to comply
Existing Plants – BATCs/BAT-AELS take effect from 10/08/22
New plants (= permit issued after 10/08/22) compliance with BATCs/ BAT-AELs required straight away
BAT-AELs = BAT - Associated Emission Levels (Mandatory)
  Often expressed as a range e.g. dust 2-5 mg/Nm3
  Footnotes to aid interpretation
Additional “narrative BAT” requirements also apply e.g. monitoring, management system requirements
Notes: So, the revised BRef was published in August 2018. New plants or significant variations from that date must comply immediately but existing sites have four years to comply.
The conclusions contain numerical emission levels as well as more narrative conditions. Although emission levels are expressed as a range, this is often to account for different abatement technologies or different processes. When we set AELs we consider what optimum performance of the plant is using the technology required taking into account other factors such as distance to sensitive receptors. So for some it may be towards the bottom of the range and for some it may be nearer the top.
Narrative conclusions are also included such as the requirement to have an environmental management system or to manage elements of the process. In some cases there will be a variety of techniques that may be used to achieve the outcome.

## Slide 5
2. WT BATCs – key changes (1)
New conclusions specific to biological treatment (non-haz) and metal shredding
  BAT-AELs for emissions to water and to air from mechanical treatments of waste (shredders) and from biological treatment of waste.
Changes in BAT-AELs for existing activities
Notes: The original WT BRef was published in 2008 and didn’t cover biological treatment or metal shredding specifically since they were new activities through the 2012 Regs.
This includes introducing BAT-AELs for emissions to water and to air for these activities.
Also some BAT AELs have been changed or added for some existing activities. This may not require any action if the new limits are already being achieved but should be addressed through the gap analysis.

## Slide 6
2. WT BATCs – key changes (2)
Emissions inventory (BAT 3)
  Part of the EMS
  Waste water
  Waste gas
Characteristics of waste inputs as well as waste water and waste gas streams
Identify relevant substances → monitoring programme
Notes: BAT 3 introduces the requirement to have an inventory of waste water and waste gas streams as part of the environmental management system. The theory is that identification of relevant waste water/waste gas streams is a prerequisite for efficient waste water/waste gas management and for the reduction of emissions by technical and management measures.
The level of detail and nature of the inventory will generally be related to the nature, scale and complexity of the installation, and the range of environmental impacts it may have (determined also by the type and amount of wastes processed).
Characteristics of waste treatment process and waste inputs:
Process flow showing sources of emissions
Treatment at source
Waste water characteristics:
Average values and variability of flow and temperature
Average concentration and load values of relevant substances and their variability, e.g. COD, TOC, nitrogen species, Phosphorus, metals, priority substances, micropollutants
Waste gas characteristics
Average values and variability of flow and temperature
Average concentration and load values of relevant substances and their variability, e.g. organic compounds, POPs, bioaerosols
Presence of other substances that may affect the waste gas treatment system or plant safety, e.g. ammonia concentration in inflow to a biofilter, dust, vapour, oxygen
For some parameters, such as cyanide and metals, monitoring is required only if the substance is identified in the inventory. This is to ensure plants don’t have to test for things that aren’t there.

## Slide 7
3. How permit reviews will work a) Permit review mechanism and timescale
Standard Further Information Notice (Regulation 63(2)) issued October 2022
Complete BAT Gap Analysis by 4 December 2022
  Not Yes/ No – looking for appropriate amount of justification and supporting evidence (in appendices) where necessary
SEPA will review Permit and may issue new consolidated variation or short variation (depending on age of Permit and degree of changes made)
  Opportunity to comment on draft variation & ELVs prior to issue
  Upgrade conditions likely
DEROGATION QUERIES – PLEASE RAISE THESE ASAP!
Reviews to be completed by end March 2023.
Notes: This is the process of carrying out the review, starting from the information notice and ending up with a reviewed permit.
You will all have received a notice with a spreadsheet to use to record performance against each relevant BAT conclusion. The level of detail needed will depend very much on the complexity of the waste treatment process carried out on site.
These must be returned to SEPA by 4th December. Obviously if the work is completed, we’d be happy to receive it before this date. To meet a deadline agreed with the Scottish Government, we are working to tight timescales. Given the volume of permits to be reviewed we are unable to offer extensions. The eight-week window should allow sufficient time to provide a full and comprehensive response. You don’t have to be in full compliance by the 4th December- just tell us how your site compares against each conclusion. If you don’t have the information, please tell us this as well. If there is additional support that we can provide to help you meet the deadline, please get in touch via the BREF e-mail address.
In a very few cases the review won’t result in any changes to the permit but for most, there will need to be a variation issued. Depending on the amount of change, this could be only a couple of conditions. Some sites will see a consolidated permit which will include historical variations. Due to the tight timescales, we accept that sites may not be in full compliance by the end of March so it is likely that there are upgrade conditions included. The timescale for these will depend on the scale of the action needed.
It is intended that site operators will have the opportunity to see the draft permit before it is issued. In order to do this we need detailed information and evidence supporting each relevant conclusion as early as possible.
If you think that the conclusion should not apply to you, or that you need a derogation from an emission limit, please contact us as early as you can. Derogations are complex to process and are only really used as a last resort and can be granted only if on-site operations are considered BAT. In many cases derogations are only a temporary measure which last as long as necessary to allow the operator to make the necessary upgrades to their installation and bring emissions to within the BAT-AEL range. Further guidance is available on our website- look for IED-TG-44.
As with all variations, operators have a right to appeal conditions.

## Slide 8
3. How permit reviews will work
b) Response to Reg 63(2) Notice and BAT Gap Analysis
For each BATC - show how you meet (or will meet) BAT
Additional tab of BAT Gap Analysis to be completed for:
  Site Baseline Report
  Relevant Hazardous Substances
Don’t refer to info already supplied to SEPA – please provide this again
If section or BATC is not applicable provide brief explanation why
Think about sensitivity of the information supplied – mark appropriately & provide justification if necessary to provide this type of information.
Notes: We are looking for detailed information on performance against each conclusion. The more detailed information we get and the earlier we get it, the easier the review will be and it’s less likely we need to bother you more than necessary.
Due to our cyber attack, we don’t have access to a lot of electronic information that was previously submitted. It is also likely that the person doing the review isn’t the normal SEPA officer and they don’t have access to paper files or works from a different office. Information may have been updated since it was originally submitted, such as recent monitoring results or an updated management plan. If there is information to demonstrate compliance please send it in, even if you have sent it already.
We have systems in place to manage large files, and sensitive or commercial information will be handled according to our policy.

## Slide 9
3. How permit reviews will work
b) Response to Reg 63(2) Notice and BAT Gap Analysis
Gap analysis spreadsheet
  Guidance tab
  General site info
  Main BAT conclusions
  BAT 7, 8 20, 21
  Site condition and baseline report
Notes: Guidance:
Links to documents
What is covered and what isn’t
What parts to complete
General site info:
Main activity from drop-down: these numbers relate to the 2012 activities. If you have a 2000 permit, you will need to pick the relevant one from the list.
Specific process is how the BRef groups the activities. You may carry out more than one of these.
Also indicate if you discharge to sewer. This flags up that you need to complete the tabs for BAT 20
Main conclusions
Work your way down the list selecting the appropriate responses
Once you have filled in the relevant rows the box should change from red to green.
BATs 7 and 8: these are about how often you monitor emissions to water and air and what to monitor for. Some of the parameters are only required where they are identified in the water or air stream.
BATs 20 and 21: these are for water discharges, one for discharges directly to a watercourse and one for discharges to sewer. Again some of these only apply where they are present in the water discharge.
The final tab is concerned with the site conditions and baseline report. It your site was permitted after 2013 then it is likely that this was done and you need to dig it out, check it is still relevant and sent it in. If you don’t have a site condition report then say so. You will need to do one but it is likely to be part of an upgrade condition. Section 2 is concerned with the use of hazardous substances on site. This isn’t just hazardous wastes but includes chemicals used at any stage in the process, including cleaning and it includes fuels if used on site. What we are looking for is whether any of these could have got into the soil or groundwater.
The final box will record whether your reports are adequate and need no further action, whether a new report will be submitted as part of the analysis, or whether more time is needed.

## Slide 10
3. How permit reviews will work
c) Unconstructed or mothballed sites
Options are:
  1. Full Permit Review (default where Notice response received)
  2. Permit Surrender (requires an application)
  3. Vary to include pre-operational condition preventing operation until compliance with BATCs and BAT-AELs demonstrated
Mothballed/ permanently closed sites – ELVs based on BAT-AELs (existing sites)
Sites which are not yet constructed – ELVs based on New Plant ELVs unless unreasonable e.g. EPC contract signed / final design reached
Relevant operators should state their intentions re Options 1-3
Notes: What if the site hasn’t been built yet but a permit is in place? Or Isn’t operating at the moment? We expect there are very few sites in this situation.
There are various options depending on the individual circumstances. Where existing sites are mothballed we are likely to carry out a review. If the site has not yet been constructed it is likely that it will be viewed as a new site unless construction is so far along that these are not possible.

## Slide 11
3. How permit reviews will work
d) SEPA WT BATC Interpretation Document
Clarifies the position of SEPA where there is flexibility in implementation or further detail is required
Additional information where necessary
Covers both new and existing plants
Informal consultation held August 2022
Could be subject to further minor changes or additions
Operators should consider the Interpretation Document when preparing their responses to the Reg 63(2) notices in the BAT Gap Analysis
Notes: SEPA has prepared an interpretational guidance document to help in the review process. Hopefully it clarifies key issues and provides further detail on what information is necessary to demonstrate compliance.
We circulated it to a few key trade bodies in August and are very grateful for their feedback. It is very much a living document and may be updated if necessary. We will also develop a FAQ section on the website if this becomes necessary.

## Slide 12
3. How permit reviews will work
e) Key differences between SEPA & EA/NRW
SEPA is aligned with other UK Regulators for majority of requirements. Key differences are:
ELVs assess performance against BAT-AEL range
  Many ELVs likely to be at top of the range but not automatic
Energy Efficiency
  SEPA Thermal Treatment of Waste Guidelines (TTWG) 2014 targets apply in addition to BAT-AEELs
Conditions and format of Permit is different
Notes: SEPA was part of both the UK shadow group and the delegation to Europe to take part in the review process. We continue to work with other regulators to ensure consistency where possible but there may be minor differences in the way we assign ELVs or implement thermal treatment efficiency.
Although wording and layout of permits will vary between regulators, they should all have the same basic requirements at the core.
You must remember that even if it’s not mentioned in the permit, you still have to meet BAT. It is a condition of having a permit that you comply with BAT.

## Slide 13
3. How permit reviews will work
f) New Permit Template and Other Changes
Conditions to be added to Permits
Those required to achieve BATC compliance including new ELVs and new monitoring requirements
Requirements for odour, noise or dust management plans where relevant
Resource efficiency
New Permit Templates
Still being drafted:
  Likely to be based on most recently issued Permits
Notes: After reviewing the spreadsheet information and the current permit we may need to add conditions to implement specific conclusions.
We are working on new permit templates and these are likely to be based on recent permits.

## Slide 14
4. QUESTION AND ANSWER SESSION
Please submit your question via the chat function
We will do our best to answer as many questions as possible on the call
Common Q&As will be added to our website
Notes: We won’t be able to go into specific issues on specific sites- these should be e-mailed to us and we will get back to you.

## Slide 15
FURTHER INFORMATION
Website: Waste Treatment Best Available Techniques (BAT) | Scottish Environment Protection Agency (SEPA)
E-mail: BREFReviews@sepa.org.uk